## Slide 1
7 April 2017
RQVX CFD Efforts
Austin Buscher, Capt, USAF
Aero Validation Branch
AFRL/RQVX

## Slide 2: Capabilities
Provide quick-turnaround simulation of aerodynamic phenomena to decrease risk and increase intuition in support of RQVX Wind Tunnel tests.
Current Capabilities
  2D and 3D Freestream flow at Mach=0.05 – 3.0
    Rakes, wings, full aircraft, etc.
  Model in SARL at Mach=0.1 – 0.5
    Floor mounted with mixed success
  Model in TGF at Mach=0.2 – 0.8
  Running “in-tunnel” CFD much more computationally intensive
Future Capabilities
  Model in VWT
  TGF at supersonic Mach (need geometries of nozzle blocks)
  Project Duration time (assuming half-time work from engineer)
    2D Freestream: 1 week
    3D Freestream: 2 weeks
    3D “in-tunnel”: 1 month

## Slide 3: Ongoing and Completed Projects
12 Projects from 2014-2017
[FS, VWT] Solid Wing (briefed SATA/STAI)
[FS] Ogive Shock Reflections
[TGF] Ogive Subsonic Blockage
[FS] Compliant Wing
[FS] Endplate Effectiveness
[SARL] Laminar Wing
[FS] SARL Rake 1
[FS] SARL Rake 2
[FS] VWT Rake
[FS] Five-Hole Probe (ongoing)
[FS] TGF Rake
[FS] RAWS Blockage Drag Estimate
First word indicates the tunnel used (internal flow) or freestream (external flow)
Abbreviations:
  FS: Freestream
  TGF: Trisonic Gasdynamic Facility
  SARL: Subsonic Aerodynamic Research Lab
  VWT: Vertical Wind Tunnel

## Slide 4: SARL Rake 1: Setup
Customer: O’Diam
Engineer: Buscher/Keane/Chang
Objective:
  Assess the rake’s aerodynamic influences pressure profiles across the length of the rake
  Compare to AEDC CFD and SARL data (to validate CFD)
  Compare old and new rake data

## Slide 5: SARL Rake 1: Results
Determined significant aero impact from rake
  Aided in design of new rake
Closely matches wind tunnel data
Supports suspicion of Mach number calculation errors in tunnel
Old Rake
New Rake
Tunnel
CFD
Very Old Rake

## Slide 6: SARL Rake 2: Setup
Customer: O’Diam
Engineer: Buscher
Objective:
  Determine suitability of Rake setup for determining flow uniformity in tunnel

## Slide 7: SARL Rake 2: Results

## Slide 8: VWT Rake: Setup
Customer: Chang
Engineer: Keane
Objective:
  Assess the rake’s aerodynamic influences
  Compare experimental data in the SARL to the CFD data we obtained

## Slide 9: VWT Rake: Results

## Slide 10: VWT Rake: Results

## Slide 11: VWT Rake: Results

## Slide 12: TGF Rake: Setup
Customer: Semmelmayer
Engineer: Buscher
Objective:
  Investigate “reverse boundary layer” that concerned PE during the TGF Checkout (May 2016)

## Slide 13: TGF Rake: Results

## Slide 14: TGF Rake: Results

## Slide 15: TGF Rake: Results

## Slide 16: Five-Hole Probe: Setup
Customer: Semmelmayer
Engineer: Chang/Buscher
Objective:
  Determine “bias” caused by addition of cone in calibration of 5-hole probes

## Slide 17: Five-Hole Probe: Results

## Slide 18: Five-Hole Probe: Results

## Slide 19: Five-Hole Probe: Results